## Slide 1: Reasoning about System Performance
CS 240: Computing Systems and Concurrency
Lecture 18
Marco Canini

## Slide 2: Context and today’s outline
We cared a lot about:
  Are the results correct?
But in practice we also need to consider quantitatively:
  Are the results obtained in a reasonable time?
  Is a system faster than another one?
Today— How to analyze the performance of a system?

## Slide 3: What’s systems performance?
The study of an entire system, including all physical components and the full software stack
Include anything that can affect performance
  Anything in the data path, software or hardware
  For distributed systems, this means multiple servers
System Under Test
Input
(Workload)
Resulting Performance
Perturbations

## Slide 4: Some terms
Workload
  The input to the system or load applied
Utilization
  A measure of how busy a resource is
  The capacity consumed (for a capacity-based resource)
Saturation
  The degree to which a resource has queued work it cannot service
Bottleneck
  A resource that limits the system performance

## Slide 5: More terms
Response time (also latency at times)
  The time for an operation to complete
  Includes any time spent waiting (queuing time) and time spent being serviced (service time), and time to transfer the result
Input
Response Time
Output
Queue
Server

## Slide 6: Who in interested?
Many roles:
  Sys admins / capacity planners
  Support staff
  Application developers
  DB / Web admins
  Researchers
  Performance engineers (primary activity)

## Slide 7: Performance evaluation is an art
Like a work of art, a successful evaluation cannot be produced mechanically
Every evaluation requires an intimate knowledge of the system and a careful selection of methodology, workloads and tools
Performance is challenging

## Slide 8: Performance is subjective
Is there an issue to begin with? If so, when is it considered fixed?
Consider:
  The average disk I/O response time is 1 ms
Is this good or bad?
Response time is one of the best metrics to quantify performance; the difficulty is interpreting its information
Performance objectives and goals need to be clear
  Orient expectations as well as choice of techniques, tools, metrics and workloads

## Slide 9: Systems are complex
Many components and sources of root causes
Issues may arise from complex interactions between subsystems that operate well in isolation
  Cascading failures: when one failed component causes performance issues in others
Bottlenecks may be complex and related in unexpected ways
  Fixing one may simply move the bottleneck elsewhere
Issue may be caused by characteristics of workload that are hard to reproduce in isolation
Solving complex issues often require a holistic approach
  The whole system needs to be investigated

## Slide 10: Example of cascading failure
Upstream service
August 2014 outage
One request type was accessing a single slow database and exhausted an upstream service’s thread pool
This starved other unrelated requests… causing widespread application unavailability
Front end service
Front end service
Front end service
Database
service
Database
service
Database
service
App 1
App 2
Workflow
Workflow
App 3
x10

## Slide 11: Measurement is crucial
You can’t optimize what you don’t know
Must quantify the magnitude of issues
Measuring an existing system helps to see its performance and perhaps the room for possible improvements
Need to define metrics
Know your tools!
Be systematic!
Don’t reinvent the wheel!

## Slide 12: Measuring Distributed Systems
Client 1
Client 2
Client N
Distributed System

## Slide 13: Measuring Distributed Systems
Client
Distributed System

## Slide 14: Latency
The time spent waiting
  E.g., setup a network connection
OR (broadly)
The time for a request/operation to complete
  E.g., an RPC, data transfer over the network, a DB query, a file system write
Measured externally from time request is sent until time response is received
Can allow to estimate maximum speedup
  E.g., assume the network had infinite capacity and transfer were instantaneous, how fast would the system go?

## Slide 15: Latency, Measure Externally
Client
Distributed System

## Slide 16: Latency, Reason Internally
Client
Single Machine
Server

## Slide 17: Latency, Reason Internally
Client
Single Machine
Server
1
2
3
Latency = 1 + 2 + 3

## Slide 18: Throughput
The rate of work performed: how many operations per unit time (ops/s) a system can handle
  In communication:
    Data rate: bytes per second, bits per second
    (Goodput useful throughput: rate for the payload only)
  Systems:
    Operation rate: ops per second, txns, per second
  IOPS
    Input/output operations per second
      E.g., reads and writes to disk per second
Measured externally as the rate that responses come out of the system

## Slide 19: Max Throughput Example (Not Ideal)
Client
Single Machine
Server
Throughput = Number of (valid) responses received by all clients
End time – start time

## Slide 20: Queuing Delay & Overload
Client
Single Machine
Server
Queuing delay: extra latency spent in queue(s)
Higher load  increase in latency
Overload: offered load > max system throughput
  Queues get really long
  Other weird/bad things happen
  Observed throughput < max system throughput

## Slide 21: Utilization, Saturation
Utilization
Load
Saturation
100%
0%
Utilization (time-based) = B/T
B is amount of time the resource was busy during T
Intuitively, how busy a component is

## Slide 22: Performance degradation
Load
Response Time
Linear
Actual

## Slide 23: Measuring Throughput Method
Starting with low load
Increase load
Repeat until measured throughput stops increasing

## Slide 24: Throughput, Reason Internally
Client
Single Machine
Server

## Slide 25: Throughput, Reason Internally
Client
Single Machine
Server
1
2
3
Throughput = min(1, 2, 3)

## Slide 26: Throughput Bottlenecks (simplified)
Client
Single Machine
Server
1
2
3
Max throughput limited by some bottleneck resource:
  Incoming bandwidth
  Server CPU
  Outgoing bandwidth

## Slide 27: Load Generation
Closed-loop
  Each “client” sends one request, waits for the response to come back, and then sends another request
  More “clients” => more load
Open-loop
  Load is generated independently of the response rate of the system, typically from a probability distribution
  More directly control the load on the system
Which one is more realistic?
We’ll reason using closed-loop clients

## Slide 28: Mental Experimental Setup
Start with 1 closed-loop client
  Expected latency?
  Expected throughput?
Double number of closed-loop clients
  Expected increase in latency?
  Expected increase in throughput?
Repeat

## Slide 29: Throughput-Latency Graph Simple Setting: Single Server; Client-Server RTT 90ms; Server Processing latency 10ms; Single-Threaded Server (100 ops/s)
Latency (ms)
100
10
20
40
100
Throughput (operations/sec)
Notes: Will mostly avoid back-of-the-envelope calculations and use of specific numbers for this class. That’s a related, important skill!

## Slide 30: Throughput-Latency Graph
Latency
Throughput
Underloaded
Overload
Common operating point:
70-80% max load
Notes: Aside:
1) Underloaded system is a waste of resources (e.g., money, energy);
2) Common operating point is 70% max load: good latency/throughput tradeoff still & can handle load spikes (organic or from failure)

## Slide 31: Throughput / Latency Relationship
Proportional at low load … but not high load
Because measured throughput is a function of latency
  i.e., throughput bottleneck is offered load
Related, but you should reason about both
For system A vs system B, all are possible:
  A has lower latency and higher throughput than B
  A has lower latency and lower throughput than B
  A has higher latency and lower throughput than B
  A has higher latency and higher throughput than B

## Slide 32: Scalability
Throughput
Load
Saturation
Knee point: beyond it, contention for resources increases; a component becomes 100% utilized
Linear
Actual

## Slide 33: Evaluation in Minutes not Months
Reasoning using your mental model is much much faster than really doing it
What would happen if?
  I moved my servers from the San Jose datacenter to Oregon?
  I switch from c5.xlarges to c5.24xlarges for my servers?
  I doubled the number of servers?
  I switch from system design X to system design Y?
    replace single server with Paxos-replicated system?
    replace Paxos with eventually consistent design?
    add batching?
    replace Paxos with new variant?

## Slide 34: Let’s use these tools!

## Slide 35: Mental Experimental Setup
System A versus System B
From 1 to N closed-loop clients loading each
Compare throughput and latency

## Slide 36: Move Single Server from San Jose to Oregon (Clients in San Jose)
Latency
Throughput
Server in San Jose
Server in Oregon
Notes: us-west-1(NorCal) <-> us-west-2 (Oregon) is 25ms

## Slide 37: Replace Single Server with Paxos (Clients and servers in same datacenter, 3 replicas)
Latency
Throughput
Single Server
Paxos

## Slide 38: Paxos: 3 replicas to 5 replicas (Clients and servers in same datacenter)
Latency
Throughput
3 replicas
5 replicas

## Slide 39: Paxos: 3 replicas to 30 replicas (Clients and servers in same datacenter)
Latency
Throughput
3 replicas
30 replicas

## Slide 40: Batching
Group together multiple operations
Improves throughput, e.g.,
  Marshall data together
  Send to network layer together
  Unmarshall data together
  Handle group of operations together
Delay processing/sending operations to increase batch size
  Common way to trade an increase in latency for increase in throughput

## Slide 41: Paxos with batching (Clients and servers in same datacenter, 3 replicas)
Latency
Throughput
no batching
with batching

## Slide 42: Paxos: 3 local replicas to geo-replicated (Clients in NY; replicas in NY, Oregon, Singapore
Latency
Throughput
all local
leader in NY
leader in Singapore
Notes: Leader local vs remote
Round up latencies for simplicity
NY <-> London 100ms
NY <-> Singapore 250ms

## Slide 43: Summary
Measure distributed systems externally
Latency: how long operations take
Throughput: how many operations/sec
Reason about latency and throughput using internal knowledge of system design
  (and back-of-the-envelope calculations)
Reason about effects on latency and throughput from changes to system choice, deployment, design
  Critical tool in system design

## Slide 44: Five ways not to fool yourself or: designing experiments for understanding performance Tim Harris
https://timharris.uk/misc/five-ways.pdf

## Slide 45: Measure as you go
Develop good test harness for running experiments early
Have scripts for plotting results
Automate as much as possible
  Ideally it is a single click process!
Divide experimental data from plot data

## Slide 46: Gain confidence (and understanding)
Plot what you measure
Be careful about trade-offs
Beware of averages
Check experiments are reproducible
(Also statistics! Deal with outliers, repetitions)

## Slide 47: Include lightweight sanity checks
It’s easy for things to go wrong… and without noticing…
Make sure you catch problems
Have sufficiently cheap checks to leave on in all runs
Have sanity checks at the end of a run
And don’t output results if any problem occurs

## Slide 48: Understand simple cases first
Start with simple settings and check the system behaves as expected
Be in control of sources of uncertainty to the largest extent possible
  And use checks to detect if that assumption does not hold
Simplify workloads and make sure experiments are long enough
Use these as a performance regression test for the future

## Slide 49: Look beyond timing
End to end improvements are great but are they happening because of your optimization?
Try to link differences in workloads with performance
Look further into differences in resource utilization and statistics from performance counters

## Slide 50: Toward production setting
Do observations made in simple controlled settings hold in more complex environments?
If that is not true, try to decouple a number of aspects of this problem
Change one factor at a time
Try to understand the differences

## Slide 51: Document results
You will forget!
  What did that experiment produce?
  Where did I see that result?
Pick a good convention to save data
Use non destructive approaches
Write summary of observations and possible explanations
  Recall: our objective is better understanding
Pick a good tool for experimenting, documenting and sharing
  Try Jupyter

## Slide 52
Final exam: Thu 12/04, 2:30-3:45PM, 9-4225
Please fill in course feedback